## Slide 1
Eshan College of Engineering
Department of Mechanical Engineering
Presented by
Mr. Rajan Khare
Assistant Professor
AUTOCAD Basic-I

## Slide 2: Launching AutoCad
Start
3D and CAD
AutoCad

## Slide 3: Typing Commands
Typing a Command
All AutoCAD commands can be typed in at the command line. Many commands also have one or two letter aliases that can also be typed as shortcuts to the commands.
Type the desired command at the command prompt.
Command : LINE
or
Type the command’s alias. Command: L
Press ENTER/Space to end.
Type an option at the command prompt.
TIP: Many AutoCAD commands require you to press ENTER to complete the command. You know you are no longer in an AutoCAD command when you see a blank command line.
Reissuing the Last Command
The last used AutoCAD command can be re-entered by one of the following three methods of ENTER. The ENTER key on the keyboard will always act as ENTER, the SPACEBAR and RIGHT MOUSE will act as enter most of the time (exceptions include placing TEXT).
Press the ENTER key on the keyboard or
Press the Space bar on the keyboard. or
Click the right mouse button.

## Slide 4: Pointing Device (Mouse)
AutoCAD uses either a mouse or digitizing tablet to select objects in a drawing.
Left Mouse Button
Used to pick or select objects
Click the left mouse button to select an object area in the drawing.
Press ESC twice to deselect an object (or to cancel a command).
Right Mouse Button
Used to enter a command, repeat last command, or access shortcut menus.
1. Click the right mouse button.
TIPS:
SHIFT + the right mouse button brings up the object snap menus.
Various screen locations for the mouse brings up different menus.• menus.

## Slide 5
5.2 PAN
Shifts the location of a view.
1. Choose
View, Pan.
or
2. Click
the Pan icon.
or
PAN from the command prompt. Command: PAN or P
3. Type
TIPS:
- While in the PAN command, click with the right mouse button to see the following menu.
- Panning can also be done by using the window scroll bars

## Slide 6
5.1 ZOOM
Increases or decreases the apparent size of objects in the current viewport
1. Choose
View, Zoom.
or
a Zoom icon.
or
ZOOM at the command prompt. Command: Zoom or Z
One of the following zoom options:
2.
Click
3.
Type
4.
Type
The following are basic zoom options:
All
Places entire drawing (all visible layers) on display at once. Forces a regeneration.
Displays current drawing content as large as possible. Restores previous view.
Designates rectangular area to be drawn as large as possible.
Extents Previous Window
Number Number X Center Dynamic
Magnification relative to ZOOM All display Magnification relative to current display (1X) Specifies center point and new display height.
Permits you to pan a box representing the viewing screen around the entire generated portion of the drawing and enlarge or shrink it.
TIPS:
-While in the ZOOM command, click with the right mouse button to see the menu to the right.

## Slide 7
2.2 Creating a New Drawing
NEW Command
Creates a new drawing file.
1. Choose
File, New.
or
CTRL + N
or
the New icon.
or
NEW at the Command prompt. Command: NEW
One of the options for creating a new drawing. The OK button.
the drawing as another name.
2.
Press
3.
Click
4.
Type
5.
6.
7.
Choose Click Save
TIP:
New drawings can also be created from Template Files.

## Slide 8
1.11 Undo and Redo
Reverses the last action.
Choose Edit, Undo. or
Click the Undo icon.
or
Press CTRL + Z.
Type U at the command prompt to undo the last command. Command: U
Redo
Reverses the effects of a single UNDO or U command.
1.
Choose Edit, Redo.
or
Click the Redo icon.
or
Type REDO at the command prompt to redo the last undo command. Command: REDO
2.
3.
TIPS:
-UNDO has no effect on some commands and system variables, including those that open, close, or save a window or a drawing, display information, change the graphics display, regenerate the drawing, or export the drawing in a different format.
-REDO must immediately follow the U or UNDO command.

## Slide 9
1.12 Function Keys and Accelerator Keys

## Slide 10
2.1 Open Existing Drawings
1. Choose
File, OPEN.
or
2. | Press | CTRL + O.
 |  | or
3. | Click | the OPEN icon.
 |  | or
4. | Type | OPEN at the command prompt.
 |  | Command: OPEN
5. | Press | ENTER
6. | Double Click | the desired directory to find the drawing to open.
7. | Click | the drawing name to open.
8. | Click | The OK button.
TIP:
-Preview shows a bitmap image of the drawing selected. This image is the view that was last saved in the drawing. It will not show a preview of drawings saved before R13 AutoCAD.

## Slide 11
Quick Save
The QSAVE command is equivalent to clicking Save on the File menu.
If the drawing is named, AutoCAD saves the drawing using the file format specified on the Open and Save tab of the Options dialog box and does not request a file name. If the drawing is unnamed, AutoCAD displays the Save Drawing As dialog box (see SAVEAS) and saves the drawing with the file name and format you specify.
1. | Press | CTRL + S.
 |  | or
2. | Click | the Save icon.
 |  | or
3. | Type | QSAVE at the command prompt,
 |  | Command:QSAVE
TIPS:
Drawings can be saved as different versions of AutoCAD (e.g. R13, R14, R 2000, etc.)
AutoSave settings under Tools, Options…

## Slide 12: Useful Commands

## Slide 13
7.1 Running Object Snaps
An object snap mode specifies a snap point at an exact location on an object. OSNAP specifies running object snap modes, which remain active until you turn them off.
1. Choose
Tools, Drafting Settings...
or
DDOSNAP at the command prompt Command: DDOSNAP
or
OSNAP on the Status Bar.
2.
Type
3.
4.
5.
Click
Right Click the Object Snap TAB.
Choose
an object snap to turn ON/OFF from the dialog box.

## Slide 14
AutoCAD 2D Tutorial
UNITS Command 8.5
1.
Choose
Format, Units... or
DDUNITS at the command prompt.
Command: DDUNITS or UN
a units and angle setting. a precision setting.
2.
Type
3.
4.
Choose Choose
- 58 -

## Slide 15
3.1 Line Command
Creates single straight line segments
1. Choose
2.
Click
Draw, Line.
or
the Line icon.
or
LINE from the command prompt Command: LINE or L
ENTER
From point: (point)
Specify next point or [Close/Undo]:(point) Specify next point or [Close/Undo]:(point)
ENTER to end line sequence
or
U to undo the last segment To point: U (undo)
or
C to create a closed polygon To point : C (close)
3.
Type
4.
5.
6.
7.
8.
Press Pick Pick Pick Press
9.
Type
10. Type
TIPS:
You can continue the previous line or arc by responding to the From point: prompt with a space or ENTER.
Choose the right mouse button for the line pop-up menu to appear while in the line command

## Slide 16
AutoCAD 2D Tutorial
Pline Command 15.1
A polyline is a connected sequence of line segments created as a single object. You can create straight line segments, arc segments, or a combination of the two.
1.
Choose
Draw, Polyline.
or
the Pline icon.
PLINE at the command prompt Command : PLINE or PL
A point on the drawing to start the polyline From point:(select)
One ofthe following options Arc/Close/Halfwidth/Length/Undo/Width/<endpoint of line>:
2.
3.
Pick Type
4.
Pick
5.
Type
or
A point to continue drawing Arc/Close/Halfwidth/Length/Undo/Width/<endpointof line>: (pick point)
6.
Pick
Polyline as one segment
- 128 -

## Slide 17
3.4 Orthogonal Lines
Controls lines from being drawn at various angles to straight lines. When the snap grid is rotated, ortho mode rotates accordingly.
1. | Press | Function Key F8.
2. | Double Click | or ORTHO from the Status Bar.
3. | Press | or CTRL + L.
Line drawn
with ORTHO ON
Line drawn with ORTHO OFF

## Slide 18
AutoCAD 2D Tutorial
Rectangle 16.2
1. Choose
Draw, Rectangle.
or
the Rectangle icon.
or
Rectang at the command prompt Command: RECTANG Chamfer/Elevation/Fillet/Thickness/Width/
<First corner>:
first corner.
other corner or type coordinates (i.e. @4,2).
2.
Click
3.
Type
4.
5.
Pick Pick
- 137 -

## Slide 19
3.6 Circles
Circle Command
1.
Choose
2.
Click
3.
Type
4.
Type
Circle, Center Radius
Circle, Center Diameter
Circle, Tangent, Tangent Radius
Circle, Tangent, Tangent, Tangent
Draw, Circle.
or
the Circle icon.
or
CIRCLE at the command prompt. Command: CIRCLE
One of the following options: 3P/2P/TTR/<<center point>>:
or
A center point.
A radius or diameter.
or
5.
6.
Pick Type
7.
Pick
A radius or diameter Diameter/<<radius>>:
TIPS:
To create circles that are the same size, press ENTER when asked for the circle radius.
When selecting a circle with a pickbox, be sure to select the circumference of the circle.

## Slide 20
  Arc Command
    Choose
Draw, Arc.
or
2.
Click
the Arc icon.
or
ARC at the command prompt Command: ARC
One of the arcs.
3.
Type
4.
Draw
TIPS:
-Except for 3 point arcs, arcs are drawn in a COUNTERCLOCKWISE direction.
- While in the arc command, press the right mouse button to select the following options for arcs:
Arc Examples
3 point arc
Start ,center, chord length
start, center, end
Start, end, radius
Start , center, included angle
Start, end, direction

## Slide 21
AutoCAD 2D Tutorial
Spline 16.3
The SPLINE command creates a particular type of spline known as a nonuniform rational B-spline (NURBS) curve. A NURBS curve produces a smooth curve between control points
1. | Choose | Draw, Spline.
2. | Click | or the Spline icon.
 |  | or
3. | Type | SPLINE at the command prompt
 |  | Command: SPLINE
4. | Pick | A start point for the spline
 |  | Object / <Enter first point>: (pick point)
5. | Pick | Points until youare done drawing splines
 |  | Enter point:(pick points)
6. | Press | Enter or close to complete the spline
7. | Pick | Starting tangentpointforthe spline
 |  | Enter start tangent (pick point)
8. | Pick | Ending tangent pointforthe spline
 |  | Enter end tangent: (pick point)
- 138 -

## Slide 22: Editing

## Slide 23
AutoCAD 2D Tutorial
Editing Polylines 15.2
1. | Choose | Modify, Polyline.
 |  | or
2. | Pick | the Pediticon from the Modify II toolbar.
3. | Type | PEDIT at the command prompt
 |  | Command: PEDIT
4. | Pick | Pick a polyline to edit
 |  | Select Polyline:(pick)
5. | Type | One ofthe following options:Close/Join/ Width/Edit vertex/FitCurve/Spline/Curve/
 |  | Decurve/Undo/eXit
- 130 -
PEDIT options:
Close Join Width Fit curve
Closes open polyline segments
Connects polylines, lines, and arcs to existing polylines. Changes the width for all polyline segments.
Creates curved arc segments around pline vertices at the direction you specify.
Creates a curve through control points on a polyline. Straightens curved segments.
Displays the following Edit Vertex Options:
Spline Curve Decurve
Edit Vertex
Polyline width change
Splined Polyline

## Slide 24
AutoCAD 2D Tutorial Move Command 10.1
- 74 -
1. Choose
Modify, Move.
or
the Move icon.
or
MOVE at the command prompt Command: MOVE or M Objects to move
Select objects: (select) A point to move from
Base point or displacement: (pick point) A point to move to
Second point of displacement: (pick point)
2. Click
3. Type
4. Pick
5. Pick
6. Pick
Circle before move
Circle after move
TIP:
To move an object a specified distance, type a distance at the second point of displacement prompt: @1<0

## Slide 25
AutoCAD 2D Tutorial
Copy Command 10.2
- 75 -
1. Choose
Modify, Copy.
or
the Copy icon.
or
COPY at the command prompt. Command: COPY or CP
2.
Click
3.
Type
4.
Pick
Objects to copy.
Select objects: (select) A point to move from.
Base point or displacement/Multiple: (pick point). A point to copy to.
Second point of displacement: (pick point)
or
A point to copy to.
Second point of displacement: @ 1<0
5.
Pick
6.
Pick
7.
Type
Duplicate objects copied
Multiple objects copied
TIP:
To copy many objects in the same copy command, type M for Multiple at the “Base point or displacement/Multiple” option.

## Slide 26
AutoCAD 2D Tutorial
Offset Command 10.4
Offset Distance
To offset a specified distance:
- 77 -
1. | Choose | Modify, Offset.
 |  | or
2. | Choose | the Offset icon.
 |  | or
3. | Type | OFFSET at the command prompt.
 |  | Command: OFFSET or O
4. | Type | The distance to offset.
 |  | Offset distance or <Through point>: (number)
5. | Pick | The object to offset.
 |  | Select object to offset: (select object)
6. | Pick | A side to offset object to.
 |  | Side to offset: (pick side)
7. | Pick | Another object to offset
 |  | Select object to offset: (pick side)
or
Enter to end the command.
8. Press
Offsetting objects by specifying a distance

## Slide 27
AutoCAD 2D Tutorial
Explode Command 15.4
1. Choose
Modify,Explode.
or
the Explode icon.
EXPLODE at the command prompt.
Command: EXPLODE
or
The object to explode. Select objects: (pick)
2.
3.
Pick Type
4.
Pick
Polyline before explode
- 133 -
Polyline (line) after explode

## Slide 28
AutoCAD 2D Tutorial
- 79 -
EXTEND 10.5
1. Choose
Modify, Extend.
or
the Extend icon.
or
EXTEND at the command prompt Command: EXTEND
Select boundary edge(s)...
The BOUNDARY edge to extend to Select objects: (select)
ENTER to accept the boundary edge Select objects: (press enter)
The objects to extend
<Select object to extend> / Project / Edge / Undo: Select an object, enter an option, or press enter : (select)
ENTER when you are done choosing objects
2. Click
3. Type
4. Pick
5. Press
6. Pick
7. Press
Lines Extended to an Arc
(Arc is boundary edge)
TIP:
- Use the object selection option FENCE to choose multiple objects

## Slide 29
AutoCAD 2D Tutorial
Stretch 13.2
1.
Choose
Modify, Stretch. or
the Stretch icon.
STRETCHat the command prompt. Command : STRETCH Select objects to stretchby window...
C to choose CROSSING window Select objects: C
A first corner to stretch. First corner: (point)
The opposite corner to window the objects to stretch.
Other corner:(point)
2.
3.
Click Type
4.
Type
5.
6.
Pick Pick
7.
8.
Press Pick
ENTER to accept objects to stretch.
A base point to stretch from Base point: (point)

## Slide 30
AutoCAD 2D Tutorial
9.
Pick
A point to stretch to Newpoint: (point) or
A distance to stretch. Newpoint: @1<0
10. Type
TIP:
The Stretchcommand must use a CROSSING windowor aCROSSING POLYGON window.

## Slide 31
AutoCAD 2D Tutorial
TRIM 10.6
The TRIM command allows you to trim objects in a drawing so they end precisely at a cutting edge defined by one or more other objects in the drawing.
- 80 -
1. Choose
Modify, Trim.
or
the Trim icon.
TRIM at the command prompt Command: TRIM
Select cutting edge(s)...
The CUTTING edge to extend to Select objects: (select)
ENTER to accept the cutting edge Select objects: (press enter) Objects to trim
<Select object to trim> / Project / Edge / Undo: Select an object, enter an option, or press enter
ENTER when you are done choosing objects Select object to trim/Undo: (press enter)
Click
Type
4. Pick
5. Press
6. Pick
7. Press
Lines Trimmed to an Arc
(Arc is cutting edge)
TIP: Hold the SHIFT key to interactively extend instead of trim.

## Slide 32
AutoCAD 2D Tutorial
Break 13.1
1.
Choose
Modify, Break. or
the Break icon.
or
BREAK at the command prompt. Command: BREAK
Object to break.
Select object: (select one object) A second break point.
Enter second point : (point)
2.
Click
3.
4.
Type Pick
5.
Pick
or
- 112 -
6.
Type
F to choose a different break point
Enter second point (or F for first point):(F)

## Slide 33
AutoCAD 2D Tutorial
MIRROR 10.7
1. | Choose | Modify, Mirror.
 |  | or
2. | Click | the Mirror icon.
 |  | or
3. | Type | MIRROR at the command prompt.
 |  | Command: MIRROR
4. | Pick | Objects to mirror.
 |  | Select objects:(select)
5. | Pick | First point of mirror line: (point)
6. | Pick | Second point: (point)
7. | Type | Yes to delete the original objects and No to keep them.
 |  | Delete old objects? Y or N
Mirror Line
- 82 -

## Slide 34
AutoCAD 2D Tutorial
- 84 -
ROTATE 10.9
1. Choose
Modify, Rotate.
or
the Modify icon.
or
ROTATE at the command prompt Command : ROTATE
Objects to rotate:
Select objects:(select)
A pivot point to rotate around Base point: (point)
A rotation angle<Rotation angle>/Reference: (number)
or
A rotation angle<Rotation angle>/Reference: (point)
2. Click
3. Type
4. Pick
5. Pick
6. Type
7. Pick

## Slide 35
AutoCAD 2D Tutorial
SCALE 10.10
1. Choose
Modify, Scale.
or
the Scale icon.
or
SCALE at the command prompt Command: SCALE
Select objects: (select objects)
A pivot point to scale about Base point: (point)
A rotation angle<Scale factor>/Reference:(number)
or
A scale factor<Scale factor>/Reference: (point)
Scale factor/Reference: (points)
2. Click
3. Type
Pick
Type
6. Pick
- 86 -

## Slide 36
AutoCAD 2D Tutorial Text Command 11.1
Text
Creates a single-line text object
- 89 -
1. Type
TEXT at the command prompt Command: TEXT
or
the Single Line Text icon from the Text Toolbar. A start point
Justify/Style/<Start Point>: (point)
or
J to change the justification or S to change the text style.
A text height
Height <default>: (type value or pick two points) A rotation angle
Rotation angle <default>: (angle or point) A text string
Text: (type text string) enter to exit the Text: prompt.
Pick
Pick
4. Type
5. Type
6. Type
7. Type
8. Press
DTEXT (Dynamic Text)
Creates a single-line text object, showing the text dynamically on the screen as it is entered.
1. Choose
Draw, Text, Single Line Text.
or
DTEXT at the command prompt Command : DTEXT
the steps 3-8 from above.
2. Type
3. Follow

## Slide 37: Layers

## Slide 38
AutoCAD 2D Tutorial Introduction to Layers and Layer Dialog Box12.1
1. | Choose | Format, Layer.
2. | Type | or LAYER at the command prompt.
 |  | Command: LAYER (or LA)
or
the layers icon from the Layer Control box on the object properties toolbar.
3. Pick
AutoCAD 2005
Layer Properties

## Slide 39
AutoCAD 2D Tutorial Layer Options 12.2
?
Make Set
New ON OFF
Color Ltype Freeze
Thaw Lock
Lists layers, with states, colors and linetypes. Creates a new layer and makes it current.
Sets current layer.
Creates new layers . Turns on specified layers. Turns off specified layers.
Assigns color to specified layers. Assigns linetype to specified layers.
Completely ignores layers during regeneration. Unfreezes specified layers Ltype.
Makes a layer read only preventing entities from being edited but available visual reference and osnap functions.
Places a layer in read write mode and available for edits. Turns a Layer On for Plotting
Turns a Layer Off for Plotting
Controls the line weight for each layer
Unlock
Plot No Plot
LWeight
TIP:
Layers can be set using the command line prompts for layers. To use this, type –LAYER or -LA at the command prompt
Type
Type
Command: -LAYER or LA
One of the following layer options
?/Make/Set/New/ON/OFF/Color/Ltype/Freeze/Thaw:

## Slide 40
AutoCAD 2D Tutorial
Layer Shortcuts 12.3
Changing the Layer of an Object
Click
Select
Once on the object to change.
the desired layer from the Layer Control Box dropdown.
AutoCAD will move the object to the new layer.
Select layer
Select object first

## Slide 41: Colours + Line Weights

## Slide 42
AutoCAD 2D Tutorial Color Command 12.6
1. Choose
Format, Color.
or
DDCOLOR at the command prompt. Command: DDCOLOR or COL
2. Type
or
Color on the Object Properties toolbar and then select a color from the list or select Other to display the Select Color dialog box.
3. Choose
TIP:
These settings ignore the current layer settings for color.
By Layer
If you enter bylayer, new objects assume the color of the layer upon which they are drawn.
By Block
If you enter byblock, AutoCAD draws new objects in the default color (white or black, depending on your configuration) until they are grouped into a block. When the block is inserted in the drawing, the objects in the block inherit the current setting of the COLOR command.

## Slide 43
AutoCAD 2D Tutorial Linetypes 12.7
Loading and Changing Linetypes
1. Choose
Format, Linetype...
or
DDLTYPE at the command prompt. Command:DDLTYPE or LT
2. Type
3. Choose
Load... to see a list of available linetypes.
4. Choose
the desired linetype to assign.
5. Click
OK.

## Slide 44
AutoCAD 2D Tutorial Lineweights 12.8
Loading and Changing Lineweights
1. Choose
Format, Lineweight...
or
LINEWEIGHT at the command prompt. Command: LINEWEIGHT or LWEIGHT
2. Type
or
a lineweight to make current from the Object Properties menu.
4. Pick
TIPS:
Lineweights can also be assigned to layers.
The Display Lineweights feature can be turned on/off o n the status bar to show or not show lineweights in the drawing, thus making regenerations faster.
Lineweights are displayed using a pixel width in proportion to the real- world unit value at which they plot. If you are using a high-resolution monitor, you can adjust the lineweight display scale to better display different lineweight widths.

## Slide 45
AutoCAD 2D Tutorial
Object Properties 12.9
Choose
Click
Modify, Properties.
or
the Properties icon.
or
DDCHPROP or DDMODIFY at the command prompt. Command: DDCHPROP (CH) or
DDMODIFY (MO)
Objects whose properties you want to change Pick a window for DDCHPROP, single object for DDMODIFY.
Select objects:(select) ENTER to accept objects. Select objects: (press enter)
One of the following properties to change.
3.
Type
4.
Pick
5.
Press
6.
Choose

## Slide 46: Other Useful Functions

## Slide 47
AutoCAD 2D Tutorial
BHATCH Command 17.1
1. Choose
Draw, Hatch...
or
the Hatchicon.
or
BHATCH at the command prompt Command: BHATCH
2.
Click
3.
Type
- 152 -

## Slide 48
AutoCAD 2D Tutorial Measuring Distances 8.2
- 55 -
1. Choose
Tools, Inquiry, Distance.
or
the Distance icon from the Inquiry Toolbar.
or
DIST at the command prompt Command: DIST
The first point to measure from First point: pick point
The second point to measure to Second point: pick point
2. Click
3. Type
4. Pick
5. Pick
Distance Between Circle Centers
TIP:
Be sure to use Object Snaps with the MEASURE command.

## Slide 49
AutoCAD 2D Tutorial
Linear Dimensions 26.1
1 . Choose
Dimension, Linear.
or
the Linear Dimension command from the toolbar.
2 . Click
or
DIM at the command prompt. Command: DIM
Dim: HOR or VER
3 . Type
- 223 -

## Slide 50
AutoCAD 2D Tutorial
Aligned Dimensions 26.2
1 . Choose
Dimension, Aligned.
or
the Aligned Dimension command from the toolbar.
2 . Click
or
DIM at the command prompt. Command: DIM
Dim: ALIGNED
3 . Type
- 224 -

## Slide 51
AutoCAD 2D Tutorial
Radial Dimensions 26.3
1 . Choose
Dimension, Radius or Diameter.
or
the Radial Dimensions command from the toolbar.
2 . Click
or
DIM at the command prompt. Command: DIM
Dim: RADIUS or DIAMETER
3 . Type
- 225 -

## Slide 52
AutoCAD 2D Tutorial Calculating Areas 8.3
- 56 -
1. Choose
Tools, Inquiry, Area.
or
the Area icon.
or
AREA at the command prompt Command: AREA
The first point for area calculation
<First point>/Object/Add/Subtract: pick
Next point: pick
Next point: pick
ENTER when you are finished choosing points. Area of Rectangle
2. Click
3. Type
4. Pick
Pick
Pick
Press
Object
Allows user to pick an object to calculate area (circle or polyline).
Adds separate areas for a total area calculation Subtracts areas from each other.
Add Subtract
TIPS:
Be sure to use Object Snaps with the MEASURE command
To subtract an area, you must first be in “add” mode to add the first area.

## Slide 53
AutoCAD 2D Tutorial
Plot Settings
- 65 -
Choose
Choose
the Plot Settings tab.
the appropriate paper size based on the chosen plotter.
the paper units (inches or mm).
the drawing orientation (Portrait, Landscape, Upside down).
the plotting area. the plot scale.
plot to center or specify an x or y offset. OK.
Choose
Choose
Choose
Choose
Choose
Click

## Slide 54
1.13 On-Line Help
Choose Help, AutoCAD Help.
or
Click the Help icon. or
Type HELP at the command prompt Command: HELP
or
Press Function Key F1