## Slide 1: ESHAN COLLEGE OF ENGINEERING FARAH MATHURA SUB- STEEL STRUCTURE NAME- ASHISH VERMA

## Slide 2: Steel



Man made metal derived from iron- which is its major constituent
Remaining components are small amounts of other elements
Added to improve the quality of steel

## Slide 3: Used as:


Basic products of steel mill such as plate, section and bars
From this members are fabricated viz. beams, girders, columns, struts, ties etc.

## Slide 4: Steel vs. Cast Iron





Up to 1.5 % Carbon combines with iron
More than 1.5 -4.5 % present as free graphite – known as cast iron
Properties vary with the varying carbon content
Increasing carbon content produces increase in shear strength & hardness
Decreases the ductility and toughness

## Slide 5: Comparison between Cast Iron, Wrought Iron &
Steel
Comp strength
4.75 -25.2 tonnes/ sq cm
Ultimate tensile strength is 5.51 to
11.02 t /sq m
compressive strength is 2.0 tonnes/sq cm and ultimate tensile strength 3.15 tonnes/sq cm
Comp. strength
6.3-7.1 tonnes/sq cm
Ultimate tensile strength 1.26 to 1.57tonnes/sq cm.
Strength
Can be hardened & tempered
Cannot be hardened or tempered
Hard, hardened by heating & sudden cooling
Hardness
1300-1400 degree Celsius
1500 degree Celsius
1200 degree Celsius
Melting point
Midway
Purest
Contains up to 0.25% carbon
Crude form containing 2-4% carbon
composition
Cast Iron Wrought iron Steel

## Slide 6: Comparison between Cast Iron, Wrought Iron & Steel Cast Iron Wrought iron Steel
Absorbs shocks
Cannot stand heavy shocks
Does not absorb shocks
Reaction to sudden shock
Rapidly forged or welded
Easily forged or welded
Brittle and cannot be welded or rolled into sheets
Forging & Welding
Tough, malleable & Ductile
Tough, malleable, ductile & moderately elastic
Brittle & cannot be welded or rolled into sheets
Malleability&Duct ility
Rusts easily
Rusts more than Cast Iron
Does not rust easily
Rusting

## Slide 7: Comparison between Cast Iron, Wrought Iron & Steel
Used as reinforcemen t in R.B. & R.C.C.
Used in making St. members, bolts, rivets and sheets (plain and corrugated)
Making cutlery, files & machine tools
Costlier than mild steel so being replaced by the latter
Withstand shocks without permanent injury so used in chains, crane hooks and railway couplings
For parts that rust easily like water pipes, sewers, drain pipes etc.
Making such parts of machines as are not likely to be subjects to shocks or tension
Lamp posts, columns and railings
Uses
Cast Iron Wrought iron Steel

## Slide 8: Types of Steel: (According to varying Carbon Content)





Dead Mild Steel (Less than 0.15 % Carbon )
Mild Steel (0.15 – 0.30 % Carbon)
Medium Carbon Steel (0.30 -0.80 % Carbon) High Carbon Steel (0.80 -1.50 % Carbon) Cast Steel / Carbon Tool Steel (More than
1.50 % Carbon)

## Slide 9: Mild Steel










Ductile & malleable
More tough and more elastic than cast iron and wrought iron More prone to rusting than wrought iron
Corrodes quickly
Easily forged, welded & riveted Withstands shocks & impacts well Not much affected by saline water
Equally strong in tension, compression and in shear Difficult to harden and temper
Sp. Gravity 7.8

## Slide 10: Mild Steel : Uses





Used as rolled structural sections like I- section; T-section; channel Section; angle irons. Plates round and square rods
M.S. Round bars
Used as reinforcement in R.C.C.
M.S. tubes are used in structures
Plain and Corrugated M.S. Sheets are used in roofing

## Slide 11: Medium Carbon Steel






Granular structure
More tough & elastic than M.S. Easier to harden & to temper
More difficult to to forge and to weld
Stronger in compression than in tension or in shear
Withstands shocks and vibrations better

## Slide 12: Medium Carbon Steel : Uses


For making tools such as dills, files, chisels
Used for making those parts that ae hard , tough and durable and capable of withstanding shocks and vibrations

## Slide 13: High Carbon Steel





Increased tensile strength leads to less weight of it being used as compared to M.S.
Structure becomes lighter Resists corrosion better
Tougher and more elastic
More brittle and less ductile than mild steel