## Slide 1
ESHAN COLLEGE OF ENGG FARAH MATHURA
NAME-GANESH SINGH
SUB-CONCRETE TECHNOLOGY

## Slide 2: WORKABILITY OF CONCRETE
workability is an important property of concrete in its stage. workability in simple terms can be defined as “the ease with which the concrete can be mixed, transported, placed and compacted”. The workability of concrete has also been defined as the amount of work required to place concrete and to compact it thoroughly
The workability is associated with the following four
concepts:
.Ease of flow (internal friction) 2.Prevention of segregation 3.Prevention of harshness 4.Prevention of bleeding
2
PAGE=2

## Slide 3: WORKABILITY OF CONCRETE
workability is an important property of concrete in its stage. workability in simple terms can be defined as “the ease with which the concrete can be mixed, transported, placed and compacted”. The workability of concrete has also been defined as the amount of work required to place concrete and to compact it thoroughly
The workability is associated with the following four
concepts:
.Ease of flow (internal friction) 2.Prevention of segregation 3.Prevention of harshness 4.Prevention of bleeding
3
PAGE=2

## Slide 4: EASE OF FLOW (INTERNAL FRICTION)
The ease with which the concrete flows depends upon the internal friction between the particles of concrete. To improve workability, therefore it is necessary to reduce the internal friction. The internal friction can be reduced by the lubrication of the surface of aggregates.
The lubrication can be improved in two ways:
4
PAGE=3

## Slide 5: PAGE=4
By increasing the quantity of water in a concrete mix. Greater the quantity of water, more area it can lubricate. But this method is inefficient because it increases water-cement ratio and thereby decreases the strength of cement.
The second way is to reduce the total surface area of the aggregates by adopting coarse aggregate. But coarse aggregate should not be used too much o.therwise segregation will take place.
5

## Slide 6: SEGREGATION
4
The separation of coarse aggregate from the concrete mix in plastic stage is called segregation.
Concrete is not a homogenous material but rather a mixture of materials of different specific gravities. So there is always a tendency for the coarser and heavier particles to settle down and for lighter materials to rise to the surface.
Segregation reduces the strength and durability of concrete.
PAGE=5

## Slide 7: Causes of segregation. Segregation takes place when:
7
there is too much of water in the mix.
there are badly graded aggregates.
there are too much shocks to a concrete mix due to transport over longer distances, discharge of concrete from a considerable height (more than 1m)
, Pumping of concrete.
leakage of mortar from formwork.
concreting is done under-water.
PAGE=6

## Slide 8: Prevention of segregation.
The mix should be designed correctly and minimum amount of water should be used for mixing.
The height of free fall of concrete should not exceed 1m in any case.
The air-entraining agents should be used for reducing segregation as these reduce the quantity of mixing water.
The concreting operations should be supervised strictly.
8
PAGE=7

## Slide 9: HARSHNESS The concrete mix which does not give smooth surface with a certain amount of trowelling is known as harsh mix.
Causes of harshness.
The cement mortar not sufficient to fill the voids in the coarse aggregates.
The presence of excessive proportion of one particle-size in an aggregate grading.
Prevention of harshness. Harshness can be prevented if there is sufficient proportion of mortar to fill the voids in coarse aggregates.
9
PAGE=8

## Slide 10: BLEEDING
The appearance of water along with some particles of cement and very fine sand on the surface of freshly placed concrete after compaction is called bleeding. A good concrete should be free from bleeding. The term water gain is also sometimes used instead of bleeding when water rises to the surface, flow channels are formed in concrete mass. Thus concrete with large amount of bleeding are permeable. Due to bleeding watery scum (water+ particles of fine sand and cement) is formed on the concrete surface. This scum layer is known as laitance. This layer should be removed if a new concrete layer is to be placed over the old layer.
10
PAGE=9

## Slide 11: Causes of bleeding.
presence of excess water.
Deficiency of fine aggregate.
Too much finishing.
Prevention of bleeding. bleeding can be prevented by:
  controlling the water- content ratio
  providing finer grading of fine aggregates.
  using finely ground cement.
  contro lling compaction.
  The air-entraining agents should be used to prevent bleeding.
11
PAGE=10

## Slide 12: FACTORS AFFECTING WORKABILITY
The factors which effect the workability of concrete are:
Water content
Size of aggregate
Shape of aggregate
Grading of aggregate
Porosity and absorption of aggregate
Admixtures
Mixing time
Temperature
12
PAGE=11

## Slide 13: PAGE=12
1.Water content. Workability of concrete mix largely depends upon its water content. With the increases of water, the workability also increases. But too much water results into concrete of low strength and poor durability. 2. Size of Aggregate. Workability increases with the increase in the size of the aggregate. Large size particles provide less surface area as compared to surface area given by smaller size particles. Hence for same degree of workability, less water is required for large size aggregate. Lesser quantity of water used in large size aggregate also reduces the quantity of cement for given water-cement ratio and is therefore economical. From practical point of view, the maximum size of aggregate to be used will depend upon the handling, mixing and placing equipment, thickness of section and quantity of
reinforcement.
13

## Slide 14: PAGE=13
Shape of Aggregate. The particle shape also effect the workability. Workability increases with round and smooth surface aggregates. Crushed or angular aggregates has less workability because of higher and rough surface area.
Grading of Aggregate. The grading of aggregate has a considerable effect on workability of concrete. Grading is more important when lean mixes of high workability are required than rich mixes. For lean mixes, the grading should be continuous, whereas for rich mixes the grading should be coarse. 5. Porosity and Absorption of Aggregate. Porous and non-saturated aggregate will require more water than a non-porous and saturated aggregate. For same degree or workability, the latter will require less quantity of water.
14

## Slide 15: PAGE=14 6. Admixtures. Workability also increases with addition of admixture such as air, entraining agents which produce well dispersed air bubbles.
Mixing Time . with the increases in mixing time upto certain limit workability increases.
Temperature. The temperature at which the concrete mix is prepared also effects its workability. The slump of the concrete mix decreases as the temperature of the mix increases.
15

## Slide 16: MEASUREMENT OF WORKABILITY
14
The following are the methods of measurements of workability:
slump test
compacting factors test
vee-bee consistometer test
Slum Test The slump test was devised in U.S.A. this test can be
performed in the laboratory or at the site of work.
Apparatus. The slump test apparatus consists of steel mould in the form of a frustum of a cone. The internal dimensions of a mould are:
(i) Bottom diameter =200mm
(ii) Top diameter=100mm
(iii) Height=300mm.
The bottom and top ends of the mould are open. Thickness of the mould should not be less than 1.6 mm. for tamping the wet concrete, a tamping rod of steel (16mm in diameter, 0.6m long) is used.
PAGE=15

## Slide 17: Procedure. The following procedure is adopted for determining the slump value of concrete:
The internal surface of the mould is thoroughly cleaned and the mould is placed on a smooth, horizontal, rigid and non-absorbent surface.
The mould is held firmly in place by standing on the foot pieces before the concrete is filled in.
Concrete under test is filled in the mould in four layers. Each layer is tamped (25 times) with the help of steel rod. The stroke should be uniformly distributed.
.
PAGE=16

## Slide 18
After the top layer has been rodded, the PAGE=17 concrete should be struck off level with a trowel. Any mortar which has leaked out between the base plate and the mould is cleaned away.
The mould is then removed by raising it slowly and carefully in vertical direction. On the removal of mould, the concrete subside.
Slump is measured immediately by determining the vertical distance between the height of the mould and that of highest point of the specimen being tested
If specimen collapses than test may be repeated

## Slide 19: PAGE=18
The slump which is the subsidence of the concrete cone after the mould is lifted up can give the following three results:
True slump------ If the concrete subside evenly, it is known as true slump.
shear slump----- If one half of the concrete slides down as soon as the mould is removed.
collapse slump----- If the concrete slides down as soon as the mould is removed , it is known as collapse slump. It is very difficult to measure. It occurs in very wet mixes.

## Slide 20: PAGE=19
Degree of workability w.r.t. slump value
S.No. | Slump value in mm | Degree of workability
1. 2. 3. 4. | (compacting factor is suitable) 25-75 50-100 100-150 | Very low Low Medium High

## Slide 21: Table -2
Recommended slumps for placement in various conditions
PAGE=20
S.NO | Slump in mm | Degree of workability | Placing Conditions
1. | (compacting factor is suitable) | Very low | Blinding concrete Shallow sections Pavements using pavers
2. | 25-75 | Low | Mass concrete Lightly reinforced Floors Canal linings Strip footings
3. | 50-100 | Medium | Heavily reinforced sections in slabs,beams,walls,columns Pumped concrete Slip form work
4. | 100-150 | High | Trench fill in-situ piling

## Slide 22: COMPACTING FACTOR TEST
This test was developed by Road Research Laboratory . It is mainly used in laboratory to determine workability of concrete.
Principle. The workability of concrete has also been defined as the amount of work required to place the concrete and to compact it thoroughly. It is not easy to measure the amount of work required to fully compact it. But it is simpler to apply a standard amount of work to the concrete and to measure its degree of compaction. Work is applied by dropping the concrete through a standard height into a cylindrical container. The compaction in the cylindrical container is produced by the destruction of kinetic energy of the falling concrete. The degree of compaction is termed as compaction factor.
PAGE=21

## Slide 23
PAGE=22
Apparatus. The apparatus used for this test . The apparatus consists of two hoppers in line vertically above the cylindrical container. The dimensions of the hoppers and cylinder are as follows:
Upper hopper (A) :
Top internal diameter =254mm
Bottom internal diameter =127mm
Internal height =239mm
Lower hopper (B):
Top internal diameter =229mm
Bottom internal diameter =127mm
Internal height =229mm
Cylinder (C)
Internal diameter =152mm
Internal height =305mm
Distance between bottom of upper hopper and top of lower
hopper = 203 mm
Distance between bottom of lower hopper and top of Cylinder
=203mm

## Slide 24: Procedure. The following procedure is adopted for performing the compacting factor test.
The concrete sample is placed in the upper hopper A. 2.Then the door of hopper A is opened. The sample
drops into lower hopper B filling it to overflowing.
  The trap door of the lower hopper is then opened and the sample falls into the cylinder which is also filled to overflowing.
  The surplus cement is removed from the top of the cylinder with the help of a trowel.
  The outside surface of cylinder is wiped and cleaned.
PAGE=23

## Slide 25: 6. The cylinder is then weighed and it is recorded as weight of partially compacted concrete.
The cylinder is again filled with concrete in layers not exceeding 50 mm in thickness. Each layer is fully compacted with tamping rod.
The cylinder is again weighed after wiping and cleaning the outside surface of cylinder. This weight is recorded as the weight of fully compacted concrete.
The compacting factor is then calculated from the formula:
PAGE=24

## Slide 26: Compacting factor = wt of partially compacted conc
wt of fully compacted conc.
Degree of workability w.r.t. compacting factor
PAGE=25
S.NO. | Compacting | factor | Degree of workability
1. | 0.75to | 0.80 | Very low
2. | 0.87 |  | Low
3. | 0.935 |  | Medium
4. | 0.96 |  | High

## Slide 27: VEE-BEE CONSISTOMETER TEST
The name vee-bee is derived from the initials of V. Bahrner of Sweden who developed the test. Sometimes this test is called V-B consist meter test. Vee-bee is a good laboratory test, particularly for very dry mixes.
PAGE=26

## Slide 28
Procedure. The following procedure is adoptePdAGE=27 for performing the vee-bee consistometer test.
Sheet metal cone is filled with concrete.
The glass plate rider is then brought into position so that it is touching the top of the concrete.
The concrete cone is then subjected to vibrating action by starting the vibrator. The stop watch is started as soon as the vibrator is switched on. The concrete is allowed to spread out in the cylindrical container.

## Slide 29: 4. The vibration is until the concrete surface becomes horizontal. The time taken to attain horizontal surface is noted. The time recorded in seconds gives the degree of workability.
Suitability. This method is suitable for dry concrete having very low workability.
PAGE=28

## Slide 30: PAGE=29
Degree of workability w.r.t. Vee-Bee Seconds
S.NO. | Time in seconds | Degree of workability
1. 2. 3. 4. 5. | 20-40 10-20 7-10 3-7 1-3 | Very low Low Medium High Very High